## Slide 1: Computer ARCHITECTURE (CA)
Course Instructor
Hira beenish
Department of Computer Science

## Slide 2: Recommended Books
Computer Organization and Architecture Designing For Performance By William Stallings
Computer Systems Architecture, 3rd Edition
By M.Morris Mano; Prentice Hall International

## Slide 3: Chapters Included
1. Digital logic circuits
2. Digital components
3. Data Representation
4. Memory organization
5. Basic Computer Organization & Design →→Mid Term
6. Central processing unit
7.Pilpeline & vector processing
8. Computer arithmetic
9. I/O & O/P organization
10. 10. Multiprocessors

## Slide 4: Chapter#3 Data representation

## Slide 5: Contents
Binary Numbers
Representation of negative numbers
Fraction numbers
IEEE 745 Single Precision
Basic Conversion

## Slide 6: Binary numbers
Binary number is simply a number comprised of only 0's and 1's.
Computers use binary numbers because it's easy for them to communicate using electrical current -- 0 is off, 1 is on.
You can express any base 10 (our number system -- where each digit is between 0 and 9) with binary numbers.
The need to translate decimal number to binary and binary to decimal.
In binary system the base is 2. We have only two possible values 0 or 1.

## Slide 7: Examples: decimal -- binary
Find the binary representation of 12910.
Find the decimal value represented by the following binary representations:
  10000011
  10101010
Find the decimal number represented by 10011001 in excess notation.
    100110002 = 27 + 24 + 23 + 20 = 128 + 16 +8 +1 = 15310
  Excess value:
    excess value = 153 – 27 = 152 – 128 = 25.

## Slide 8: Representation of negative numbers
Is a representation of negative numbers possible
Unfortunately:
  you can not just stick a negative sign in front of a binary number. (it does not work like that)
  There are three methods used to represent negative numbers.
  Signed magnitude notation
  Excess notation notation
  Two’s complement notation

## Slide 9: Signed-Summary
In signed magnitude notation,
    the most significant bit is used to represent the sign.
    1 represents negative numbers
    0 represents positive numbers.

## Slide 10: Representation of negative numbers
In signed magnitude
    the left-most bit represents the sign of the integer.
      0 for positive numbers.
      1 for negative numbers.
The remaining bits represent to magnitude of the numbers

## Slide 11: Fraction Representation
To represent fraction we need other representations:
  fixed point representation
  floating point representation.

## Slide 12: IEEE 745 Single Precision
The number will occupy 32 bits

## Slide 13: Representation in IEEE 754 single precision
sign bit:
  0 for positive and,
  1 for negative numbers
8 biased exponent by 127
23 bit normalised mantissa

## Slide 14: Basic Conversion
Converting a decimal number to a floating point number.
Take the integer part of the number and generate the binary equivalent
Take the fractional part and generate a binary fraction
Then place the two parts together and normalise.
6.75 in 32 bit floating point IEEE representation:-
0 10000001 10110000000000000000000